## Slide 1
University of Rome Tor Vergata
Master’s Thesis in Energy Engineering
Health-conscious model predictive control for a residential hydrogen-based hybrid renewable energy system
Macroarea di Ingegneria
Advisor
Prof. Lorenzo Bartolucci
Candidate
Federico Donato
09-06-2022
Academic Year 2020/2021

## Slide 2
Italian energy context
Chart: Power production mix (2021)
| Italia | Eu | World
Oil | 0.0439 | 0.0271 | 0.031
Gas | 0.4969 | 0.2549 | 0.2216
Coal | 0.0501 | 0.1393 | 0.3649
Solar | 0.0864 | 0.0384 | 0.0372
Wind | 0.074 | 0.1001 | 0.0659
Hydro | 0.1577 | 0.1602 | 0.1528
Nuclear | 0 | 0.2334 | 0.0994
Other | 0.091 | 0.0466 | 0.0273
Chart: Investments 2017-2030 [Bln€]
| Residential | Tertiary | Industry | Transports | Electrical sector | Electrical system
BASE scenario | 117 | 55 | 27 | 732 | 47 | 30
PNIEC scenario | 180 | 90 | 33 | 759 | 83 | 46
Piano Nazionale Integrato per l’Energia ed il Clima - PNIEC
180 Mld€
30%
+30 GW
-7 Mtep
Cumulative investments with the «PNIEC scenario»
Growth of photovoltaic
Target of renewable energy share in the final consumption
Reduction of emissions and consumptions in the residential sector
+54%
+53%

## Slide 3
Hydrogen, Distributed Generation and Smart Grid
Bartz, Stockmar, «Staying big or getting smaller», Energy Atlas 2018: Figures and Facts about renewables in Europe
Wikipedia, “Proton-exchange membrane fuel cell”
2.4
Greater mass energy density than natural gas
No GHG emissions, just water
≤60%
High energy conversion efficiency
IRENA (2020), “Green Hydrogen Cost Reduction: Scaling up Electrolysers to Meet the 1.5⁰C Climate Goal”
359
Large-scale projects announced by the EU
435 Mld€
Planned investments to 2030
10 Mton
Expected hydrogen production to 2030 (70% green, 30% blue)*
(*) Volano gli investimenti nell'idrogeno, l'astro nascente della transizione energetica - LifeGate

## Slide 4
Power grid digitalization
Penetration of renewable sources in the energy mix
Ecological transition and energy communities
Distributed generation and smart grid
Digitalize power and industrial grid - Digital grid - Iskra
Data-driven approach and machine learning
Predictive Maintenance
Health Management
Fastness and resilience
Prosumers and bidirectional power flows
Batteries and storage systems
Hydrogen and fuel cells
Stability and flexibility
Real-time monitoring
Control algorithms and forecast systems
Upgrade in the role of TSO & DSO

## Slide 5
Target
Development of a novel model predictive control system for a hydrogen-based on-grid hybrid renewable energy system for residential purposes
Objective of health-management
Objective of increased penetration of renewable energies in the energy mix and resilience
Design parameters:
Grid fastness
OPEX
Matlab
Simulink
YALMIP
Linear programming model

## Slide 6
Linear programming algorithms in YALMIP code
YALMIP code
Parameters: data of the optimization problem
Decision variables: variables to act on in order to determine the optimal outcome
Constraints: mathematical (in)equalities to define the feasible region
Objective function: mathematical expression to maximize or minimize
Introduction to Linear Programming in Python | Towards Data Science
yalmip.github.io
Canonical form of a linear programming model
Mixed Integer Linear Programming (MILP)
Decision variables can assume both integer or real values
sdpvar
Constraints
Objective
solver
Options
Optimize

## Slide 7
Control system
Grid: max power
Battery: SoC-dependent charge and discharge power
Fuel cell: 3-state operating region
Binary variables: modellazione della logica di controllo desiderata
Instantaneous power balance
Constraints on max fuel cell power rate, min number of startups and SoC definition

## Slide 8
Control system
Simulation parameters | 
Simulation Time | 7 days
Actual simulation length | ≈ 11 hours
Time horizon | 2 days
Solver | Gurobi
Controllers | 3 (2 MPC + 1 DP)
Initial simulations | 3
Further analysis | 2
Piece-wise linearization of fuel cell’s operating efficiency, in order to address non-linear effects related to fuel cell operating points
Rising region(low load factor)
Plateau region (mean load factor)
Falling region (high load factor)

## Slide 9
Control system
1° controller – MPC1
2° controller – MPC2
3° controller – DP3
OPEX
OPEX &
Time horizon: 2 days
Optimization time step: 1 day
Time horizon: 2 days
Optimization time step: 15 minutes
Optimization time step: 20 seconds
Reference grid exchange profile
Forecast data (weather + residential load)
Updated grid exchange profile
Forecast & actual data (weather + residential load)
Real-time control actions
Actual data (weather + residential load)
Dispatching (DSO), grid fastness and reliable integration of produced renewable energy
Penalty of the energy unbalance exchanged with the grid
Penalty of energy profile deviation of battery, fuel cell and grid

## Slide 10
Control system
Component | Parameters | Value | Units of measurement
Photovoltaic PV | Installed power | 6 | 
Grid | Max power | 6 | 
Battery BESS | Nominal capacity | 8 | kWh
 | State-of-Charge top | 0.9 | 
 | State-of-Charge down | 0.1 | 
 | Initial State-of-Charge | 0.5 | 
 | Charge/discharge rate | 1 – 0.1 | 
 | State-of-Charge treshold | 0.2 | 
Fuel cell FC | Nominal power | 1.7 | kW
 | Min power | 0.425 | kW
 | Standby power | 0.17 | kW
Component | Parameters | Value | Units of measurement
Photovoltaic PV |  | 6 | 
Grid |  | 6 | 
Battery BESS |  | 8 | kWh
 |  | 0.9 | 
 |  | 0.1 | 
 |  | 0.5 | 
 |  | 1 – 0.1 | 
 |  | 0.2 | 
Fuel cell FC |  | 1.7 | kW
 |  | 0.425 | kW
 |  | 0.17 | kW
Decision variables
BESS charge power
BESS discharge power
Purchased grid power
Sold grid power
Fuel cell power
State-of-Charge
Decision variables
Cost parameters | Value | Units of measurement
Grid purchase | 0.20 | €/kWh
Grid revenue | 0.10 | €/kWh
purchase | 0.8 | €/scm
Penalty fuel cell startup | 2 | €/startup
Reference fuel cell cost | 0.186 | €
Cost parameters | Value | Units of measurement
Grid purchase | 0.20 | €/kWh
Grid revenue | 0.10 | €/kWh
 | 0.8 | €/scm
Penalty fuel cell startup | 2 | €/startup
Reference fuel cell cost | 0.186 | €
Operating costs – OPEX:
+

## Slide 11
Results introduction
Chart: Expected trend of energy unbalance exchanged with the grid as a function of forecast error
| Categoria 1
Case 1 - perfect forecast | 1
Case 2 - acceptable forecast | 10
Case 3 - incorrect forecast | 50
The predictive control system can efficiently minimize the energy unbalance with the grid compared to the reference provided at the start of the day
Up to a certain degree of error, the system is still able to contain the deviation of the actual grid exchange profile to acceptable levels
If the error is too high, the system can no longer dampen deviations and therefore tends to act on the grid profile, penalising the energy unbalance exchanged with the grid
Energy unbalance: deviation between actual exchange with the grid and the reference profile reported at the beginning of the day [kWh].
KEY PERFORMANCE INDICATOR
Trend of cumulative energy exchanged with the grid
Unbalance power trend with reference to specific time targets

## Slide 12
Performance trend as a function of forecast error
1° CASE: PERFECT FORECAST
0.015
Root mean square error (RMSE)
Actual weather and load data have small deviations (± 5%) compared to the average value correctly provided by forecasts
0.486
Average fuel cell operating efficiency
The fuel cell interventions are minimal and undemanding, so the control succeeds in maxing out the average operating efficiency
3.241
Daily average energy unbalance
[kWh/d]
The system succeeds in excellently minimizing energy unbalance exchanged with the grid
Convergence between reference and actual profile
Control efficiency for time targets ≥ 15 mins
Predictive control performance: cumulative energy exchanged with the grid
Predictive control performance: unbalance power with 1-, 2- and 4-hour targets

## Slide 13
Performance trend as a function of forecast error
2° CASE: ACCEPTABLE FORECAST
0.248
Root mean square error (RMSE)
The average predicted energy from photovoltaics is overestimated compared to actual values, while the actual load is overlapped to the predicted load
0.477
Average fuel cell operating efficiency
The fuel cell works at a higher average load factor to compensate energy for unexpected photovoltaic fluctuations
138.7
Daily average energy unbalance
[kWh/d]
The system struggles to contain the unbalance energy due to the significantly incorrect forecast system
Trade-off between max efficiency and max power
Simulation hypothesis: generation profile from photovoltaics
Predictive control performance: fuel cell operating points
Actual PV always lower than expected

## Slide 14
Performance trend as a function of forecast error
3° CASE: INCORRECT FORECAST
0.394
Root mean square error
(RMSE)
The forecast are at the same time incorrect and penalising, i.e. the actual PV is less than expected and the actual load is greater than expected
0.488
Average fuel cell operating efficiency
The fuel cell is most often found working in standby conditions, resulting in a high average operating efficiency
230.9
Daily average energy unbalance
[kWh/d]
The control cannot guarantee sufficient performance in terms of energy unbalance with the grid
Predictive control performance: battery State-of-Charge profile
Predictive control performance: cumulative energy exchanged with the grid
The actual profile diverges from the reference profile already from the first day of simulation
The battery acts heavily to cover fluctuations

## Slide 15
Performance trend as a function of forecast error
Chart: Daily average energy unbalance
| 1.4999999999999999E-2 | 0.248 | 0.39400000000000002
Serie 1 | 3.241 | 138.7 | 230.9
Colonna1 | 3.241 | 138.7 | 230.9
Chart: Expected trend of energy unbalance exchanged with the grid as a function of forecast error
| Categoria 1
Caso 1 - previsioni perfette | 1
Caso 2 - previsioni accettabili | 10
Caso 3 - previsioni errate | 50
1° CASE PERFECT FORECAST
2° CASE ACCEPTABLE FORECAST
3° CASE INCORRECT FORECAST
Parameter | 1° Case: Perfect forecast | 2° Case: Acceptable forecast | 3° Case: Incorrect forecast
, [kWh] | 8 | 8 | 8
 | 1 | 0.9 | 0.9
 | 1 | 1 | 1.1
RMSE | 0.015 | 0.248 | 
Stato medio FC | Standby | Standby | Standby
 | 0.486 | 0.477 | 0.488
, [h/g] | 6.321 | 8.643 | 8.919
, [kW] | -0.659 | -0.639 | -0.619
, [kW] | -0.656 | -0.350 | -0.138
, [kWh/g] | 3.241 | 138.697 | 230.927
Parameter | 1° Case: Perfect forecast | 2° Case: Acceptable forecast | 3° Case: Incorrect forecast
 | 8 | 8 | 8
 | 1 | 0.9 | 0.9
 | 1 | 1 | 1.1
RMSE | 0.015 | 0.248 | 
Stato medio FC | Standby | Standby | Standby
 | 0.486 | 0.477 | 0.488
 | 6.321 | 8.643 | 8.919
 | -0.659 | -0.639 | -0.619
 | -0.656 | -0.350 | -0.138
 | 3.241 | 138.697 | 230.927
-94%
-97%
+59%
+66%
Further analysis
Analysis of the effect of incorrect but not penalizing forecasts
Performance as a function of battery capacity
8 kWh 12 kWh 16 kWh

## Slide 16
Effect of incorrect but not penalizing forecasts
Parameter | 1° Case: Perfect forecast | 2° Case: Acceptable forecast | 3° Case: Incorrect forecast | Simulation 1
, [kWh] | 8 | 8 | 8 | 8
 | 1 | 0.9 | 0.9 | 0.9
 | 1 | 1 | 1.1 | 0.8
RMSE | 0.015 | 0.248 |  | 0.503
Stato medio FC | Standby | Standby | Standby | Standby
 | 0.486 | 0.477 | 0.488 | 0.498
, [h/g] | 6.321 | 8.643 | 8.919 | 6.203
, [kW] | -0.659 | -0.639 | -0.619 | -0.726
, [kW] | -0.656 | -0.350 | -0.138 | -0.717
, [kWh/g] | 3.241 | 138.697 | 230.927 | 4.154
Parameter | 1° Case: Perfect forecast | 2° Case: Acceptable forecast | 3° Case: Incorrect forecast | Simulation 1
 | 8 | 8 | 8 | 8
 | 1 | 0.9 | 0.9 | 0.9
 | 1 | 1 | 1.1 | 0.8
RMSE | 0.015 | 0.248 |  | 0.503
Stato medio FC | Standby | Standby | Standby | Standby
 | 0.486 | 0.477 | 0.488 | 0.498
 | 6.321 | 8.643 | 8.919 | 6.203
 | -0.659 | -0.639 | -0.619 | -0.726
 | -0.656 | -0.350 | -0.138 | -0.717
 | 3.241 | 138.697 | 230.927 | 4.154
Simulation hypothesis: load profile
Predictive control performance: cumulative energy exchanged with the grid
The best performance is not only achievable under perfect forecasting conditions, since the predictive control system manages to ensure optimal results even in situations of high but not penalizing error
Excellent convergence between real profile and reference: the control works well!
+103%
-97%
Increase in RMSE compared to
2° case
Energy unbalance reduction compared to 2° case

## Slide 17
Unbalance power considerations resulting from MPC2 update
The average error of MPC2 optimizations is strongly penalized as the time target increases
Influence of the chosen time step on the grid profile error reported to the DSO
Chart: Time target, [h]
| 1 h | 2 h | 4 h
Serie 2 | 1.459 | 0.6109 | 1.9847
Serie 3 | -1.9268 | -1.0926 | -2.9337
Serie 1 | -0.123 | -0.172 | -0.1975
More noticeable mid-day deviations (combined presence of pv and load)
Parametro | Valore
 | +1.4590 kW
 | -1.9268 kW
 | -0.1230 kW
 | +0.6109 kW
 | -1.0926 kW
 | -0.1720 kW
 | +1.9847 kW
 | -2.9337 kW
 | -0.1975 kW
Parametro | Valore
 | +1.4590 kW
 | -1.9268 kW
 | -0.1230 kW
 | +0.6109 kW
 | -1.0926 kW
 | -0.1720 kW
 | +1.9847 kW
 | -2.9337 kW
 | -0.1975 kW
+39.8%
+60.6%

## Slide 18
Effect of battery capacity
Parameter | 3° Case: Incorrect forecast | Simulation 2 | Simulation 3
, [kWh] | 8 | 12 | 16
 | 0.9 | 0.9 | 0.9
 | 1.1 | 1 | 1.1
RMSE | 0.394 | 0.396 | 0.393
Stato medio FC | Standby | Standby | Standby
 | 0.488 | 0.471 | 0.472
, [h/g] | 8.919 | 7.476 | 8.592
, [kW] | -0.619 | -0.572 | -0.557
, [kW] | -0.138 | -0.130 | -0.155
, [kWh/g] | 230.927 | 212.271 | 193.008
Parameter | 3° Case: Incorrect forecast | Simulation 2 | Simulation 3
 | 8 | 12 | 16
 | 0.9 | 0.9 | 0.9
 | 1.1 | 1 | 1.1
RMSE | 0.394 | 0.396 | 0.393
Stato medio FC | Standby | Standby | Standby
 | 0.488 | 0.471 | 0.472
 | 8.919 | 7.476 | 8.592
 | -0.619 | -0.572 | -0.557
 | -0.138 | -0.130 | -0.155
 | 230.927 | 212.271 | 193.008
+50%
+33%
-9%
-9%
Predictive control performance: battery State-of-Charge profile
Predictive control performance: unbalance power with 1,2 and 4-hour time targets
Approximately linear trend of unbalance energy reduction as storage system size increases
Saturation effect related to increased fixed costs
Excessive oversizing of the battery compared to actual flexibility needs
Economic trade-off between increased costs and reduced energy unbalance

## Slide 19
Conclusion
The predictive control system developed shows performance that is highly dependent on:
Accuracy of the forecast system and forecast error characteristics
Degree of system flexibility and storage system capacity
The objective of the thesis work is the development of a novel model predictive control system for the management of an on-grid hybrid reneawable energy system based on hydrogen and renewable sources for residential applications, aimed at the pursuit of 2 fundamental objectives:
Objective of penetration of renewable sources in the energy system (minimization of energy unbalance)
Objective of monitoring the health of components most sensitive to deterioration (battery and fuel cell)
Further analysis on the consequences obtained from forecast error demonstrate how the control succeeds in ensuring the desired performance even under incorrect but not penalizing forecast conditions
As the battery size increases, simulations lead to a modest reduction (9%) in energy unbalance, but the effect has a saturation dependent trade-off between increased fixed costs, battery oversizing and decreased grid penalty cost
Chart: RMSE
| 1.4999999999999999E-2 | 0.248 | 0.39400000000000002 | 0.503
Serie 1 | 3.241 | 138.697 | 230.927 | 4.154
Chart: C_BESS, [kWh]
| 8 | 12 | 16
Serie 1 | 230.927 | 212.271 | 193.008